## Slide 1
Port-Hamiltonian PINN
Cardiac Digital Twin
Research Design, Process & Results
Kwanhyeong Lee
Soonchunhyang University College of Medicine, M1
Lab Meeting | June 2026

## Slide 2
Research Motivation
Clinical Gap
Invasive hemodynamic assessment (PV loop) is gold standard but requires catheterization
Non-invasive alternatives (echo) provide incomplete picture of cardiac energetics
No existing method jointly predicts hemodynamic parameters AND energy metrics
Our Approach
Physics-Informed Neural Network (PINN) as cardiac digital twin
Port-Hamiltonian mechanics for energy-consistent predictions
MIMIC-IV: 5,851 paired echocardiograms with drug exposure data

## Slide 3
Data: MIMIC-IV Paired Echocardiography
5,851
Paired Echo Studies
33,006
Total Echos (v2)
11+13
Input + Output Features
9
Drug Classes Matched
Data Pipeline
MIMIC-IV
Echocardiography
→
PINN v4
Inference
→
Energy
Computation
→
Drug
Matching
→
pH-PINN v5
Training

## Slide 4
Research Architecture: 3-Paper Structure
Paper 1
PINN Cardiac
Digital Twin
11 echo inputs
→ 7 hemodynamic outputs
R² = 0.945–0.997
Paper 2
Treatment Response
Prediction
PSM + IPTW
Drug-specific response
Digital twin validation
Paper 3
Port-Hamiltonian
PINN (pH-PINN)
Energy-consistent
H = T + V
Drug interaction network
Target: IEEE JBHI (Journal of Biomedical and Health Informatics)

## Slide 5
pH-PINN v5 Architecture
StateEncoder
11 → 256 → 128 → 64
+ GELU + Dropout
Phase Space
q = (V_LV, V_LA, V_art)
p = (p_mv, p_ao)
aux (4 dims)
Hamiltonian
T(q,p): MLP[5,64,64,1]
V(q): MLP[3,64,64,1]
H = T + V
Dissipation R
R = LLᵀ (Cholesky)
Guaranteed PSD
5×5 symmetric
Clinical Decoder (12→64→32→7)
Ees, Eed, Ea, coupling, EDP, efficiency, tau
Energy Decoder (12→64→32→6)
H, T, V, mech_eff, VA_coupling, SW
Total Parameters: 61,169 | Training: AdamW, CosineAnnealing, 150 epochs, 23s

## Slide 6
Training Results: Test Set R²
Chart: Clinical Outputs (mean R² = 0.980)
| Ees | Eed | Ea | Coupling | EDP | Efficiency | Tau
Clinical R² | 0.9844 | 0.9912 | 0.978 | 0.9817 | 0.9568 | 0.9817 | 0.9831
Chart: Energy Outputs (mean R² = 0.974)
| H | T | V | Mech_eff | VA_coup | SW
Energy R² | 0.9869 | 0.9751 | 0.987 | 0.9349 | 0.98 | 0.9786
Overall mean R² = 0.977 | All outputs > 0.93

## Slide 7
Physics Structure Guarantees
H = T + V
MSE = 3.37×10⁻¹⁵
Machine-precision energy conservation
R ≥ 0 (PSD)
0 violations / 200
Dissipation matrix positive semi-definite via Cholesky LLᵀ
T ≥ 0, V ≥ 0
Softplus enforced
Non-negative kinetic and potential energy

## Slide 8
Temporal Validation (Prospective Proxy)
Design: Train on pre-median dates, test on post-median dates
Train: 2,488 samples | Test: 2,925 samples
Chart: 
| Ees | Eed | Ea | Coupling | EDP | Eff | Tau | H | T | V | Mech | VA | SW
Random Split | 0.984 | 0.991 | 0.978 | 0.982 | 0.957 | 0.982 | 0.983 | 0.987 | 0.975 | 0.987 | 0.935 | 0.98 | 0.979
Temporal Split | 0.973 | 0.984 | 0.975 | 0.941 | 0.928 | 0.979 | 0.979 | 0.977 | 0.96 | 0.977 | 0.881 | 0.959 | 0.959
Mean R² degradation: -0.018 | All outputs maintain R² > 0.88

## Slide 9
Drug Interaction Network
Interaction = Δ(A+B) − [Δ(A) + Δ(B) − Δ(neither)]
Non-additive energy effects quantified across 21 testable drug pairs
21
Drug Pairs Tested
52%
Synergistic
43%
Antagonistic
5%
Additive
Key Findings
Top synergy: ARB + BB (ΔH interaction = −5,059 J, 280% supra-additive)
BB = most synergistic hub (5/6 connections synergistic)
CCB = most antagonistic hub (5/6 connections antagonistic)
Clinically consistent with guideline-directed HF therapy

## Slide 10
Key Achievements
01
First Port-Hamiltonian PINN for cardiac modeling
Energy-consistent architecture with provable conservation laws
02
Machine-precision energy conservation
H = T + V enforced at MSE = 3.37×10⁻¹⁵
03
Prospective-proxy validation passed
Temporal split maintains R² > 0.88 across all 13 outputs
04
Drug interaction network from digital twin
21 pairs classified as synergistic/antagonistic/additive